## Slide 1
Status of the
Monte-Carlo work
Alexander Kiselev
09.08.2014 EIC Tracking Meeting

## Slide 2: GEM geometry in EicRoot
Basic C++ classes and geometry creation scripts are coded and available
Internal structure:
Calculations by Aiwu
Input from Kondo
Very flexible configuration
Applicable to both FLYSUB and EIC detector

## Slide 3: Application to FLYSUB
-> pretty detailed geometry description
EicRoot display

## Slide 4: GEM geometry in the EIC detector
-> same FLYSUB building blocks

## Slide 5: Tracking sandbox in EicRoot
TRK2
TRK1
TRK4
TRK3
SBS2
UVA1
-> sufficient to pin down material effects
So far: simplified geometry with realistic material description
Kalman filter code ported from HERMES is used

## Slide 6: Example: global linear fit
Simulate 32 GeV protons
Reconstruct as 3.2 TeV ones (equivalent to global linear fit)
Use all TRK & SBS for track fit; try several different resolution values
Build UVA residuals under assumption of 1 micron resolution
-> a clear mismatch between linear fit estimate and “true” resolution

## Slide 7: Example: same with the Kalman filter
Numerical estimate from the previous page:
if measured UVA residual say for 70 micron TRK&SBS trackers was ~90 microns, the conclusion from global fit would be, that UVA internal resolution is ~85 microns, while in fact it was ~70 microns (and just the global fit error estimate was underestimated)
-> Kalman filter fit does not suffer from this problem
Kalman filter fit

## Slide 8: Timelines, plans, etc
Next one-two weeks:
Finalize FLYSUB geometry description (rotated strips, etc)
Conclude FLYSUB material effects study
Right after that:
Fix EIC tracker geometry for the first physics MC production
More distant future:
Include other FLYSUB detectors (vector measurements; 3D rotations)
? Hook up FLYSUB data to the simulation framework